## Slide 1: Engineering update on mmn & eeg measures for schizophrenia(SZ) management
Emmanuel Olateju
Department of Electronic and Electrical Engineering

## Slide 2: PRESENTATION LAYOUT
Introduction
Methodology (Engineering)
Progress Report
Takeaway

## Slide 3: Introduction
Schizophrenia is a serious disorder that affects more than 1.7 million Nigerians.
An objective, simple and accurate diagnostic tool for the disorder would greatly reduce the overall cost-of-care for the disease, but the best candidates for such a test are not yet accurate enough for clinical use.
This project intends to develop new approaches and tools for the diagnosis and management of Schizophrenia.
We hope to combine some existing promising techniques within an overall framework that is unique

## Slide 4: Long-Term Goals
To determine the neuropathological basis of schizophrenia which will help with identifying possible preventive measures against this very debilitating condition.
This project will also provide baseline data on MMN and ASSR among patients with schizophrenia in Nigeria.
Correlate subtypes of schizophrenia with prognosis

## Slide 5: Specific Objectives
Determine the pattern and severity of symptoms of schizophrenia.
Develop an ensemble classifier combining mismatch negativity, Fuzzy entropy and ASSR
Acquire electroencephalography (EEG) data from a population of schizophrenia patients classified into subtypes and control subjects
Correlate the index developed in (2) with schizophrenia type and severity
Develop a prototype diagnostic system based on (4);
Assess the effectiveness of the developed system for the diagnosis of first-episode schizophrenia.

## Slide 6: Overview
Develop EEG signal acquisition system for protocol:
  Arithmetic task
  At rest
  Audio stimuli
Develop signal preprocessing system
Develop and test power spectral density algorithm
Develop and test entropy algorithm
Develop and test mismatch negativity algorithm
Develop classifier
Test classifier
Implement detector on embedded device
Methodology (Engineering)

## Slide 7: Anticipated Workflow
EEG acquisition
  Arithmetic task
  At rest
  Audio stimuli
signal preprocessing
power spectral density computation
entropy computation
mismatch negativity computation
classification
Methodology (Engineering)

## Slide 8: Workflow Architecture
Methodology (Engineering)

## Slide 9: Progress Report
EEG device evaluation
Data format evaluation
Software tools selection
Preliminary work on setting up Neuropype pipeline
Preliminary results on
  Data-preprocessing
  Spectral-domain Analysis
  BCI data

## Slide 10: EEG Device Evaluation
Available device = Contec KT88-2400
  24 channels
  1000 samples per second
  Input Impedance ≥ 10MΩ
  CMRR ≥ 90dB
Based on preliminary data analysis, data from the device have sufficient signal-to-noise ratio
Question: do we want to consider rapid-wear electrode caps?
Progress Report

## Slide 11: Data Format Evaluation
Data acquired consists of one EEG recording session.
16 channels of EEG data are used at a sampling rate of 500Hz.
Data acquired from the clinic were stored in the .edf format.
The .edf format is compact and yet explicit in storing information on EEG sessions.
The .edf format stores information on session parameters such as digitization points, sampling frequency, length of recording, stimulation channels, etc.
We have been able to store pre-processed .edf data in .xdf format as the latter is easier to process compared to the former.
Progress Report

## Slide 12: Software tools selection
Software considered for processing the acquired signals include:
  Python
  MNE
  MATLAB
  EEGLAB
  Neuropype
All of the options above except Neuropype follow a functional programming style which requires design of signal processing modules and classification modules from the base level.
Progress Report

## Slide 13: Software tools selection
Neuropype offers a graphical pipeline flow programming style, with already designed signal processing and classification modules.
Neuropype is preferred to the other options
  programming paradigm is simpler allowing us to focus on algorithm development rather than their coding
  it offers readily designed modules for biological signals processing
  allows for designing custom modules in quick and easy steps.
Ease of visualization, plotting and other existing modules also qualified the python language visualization tools for usage in certain case scenarios.
Progress Report

## Slide 14: Preliminary work (Neuropype, Python)
Progress Report

## Slide 15: Data Preprocessing
Progress Report

## Slide 16: Spectral Domain Analysis
Progress Report

## Slide 17: Spectral Domain Analysis
Progress Report
Welch PSD

## Slide 18: Spectral Domain Analysis
Progress Report
Neuropype CTWT plot

## Slide 19: Spectral Domain Analysis
Progress Report
Python CTWT plot

## Slide 20: Classifier Testing (using BCI)
Progress Report
Testing the performance of classifiers on BCI(Brain Computer Interfacing) acquired EEG data in edf / xdf formats in neuropype.
Additional EEG data were acquired using OpenBCI EEG hardware
EEG data was acquired across three subjects and contains 1000 instances equally distributed between the two target classes
EEG data is to be classified into either movement class dubbed class ‘1’ or rest class dubbed as class ‘0’
Classification results shown in the following slides

## Slide 21: Classifier Testing (using BCI)
Progress Report

## Slide 22: Classifier Testing (using BCI)
Progress Report
Class 1 covariance analysis
Class 0 covariance analysis

## Slide 23: Classifier Testing (using BCI)
Progress Report

## Slide 24: Takeaway
Software tools selected: Neuropype + python
Data acquisition tools verified: Contec, edf
Sample Neuroype pipelines built and tested
Power spectral density algorithm tested
Sample classifiers built and tested
Next steps: MMN and entropy implementation

## Slide 25: THANK YOU